## Slide 1: Lowering Melter SFC with Data-Driven Setpoints
60 TPD flint melter | Gas + barrier-boost recommender | October 2026
Target: 2% lower specific fuel consumption (SFC), glass quality held
Notes: Introduce the engagement: a data-driven recommender for the 60 TPD flint melter that tells operators what NG flow, secondary air and barrier boost to run, with the goal of a 2% lower SFC while seeds and furnace limits hold.

## Slide 2: Agenda
From the plant's question to setpoints the operator can run
01
The challenge
Problem statement, acceptance criteria, SFC formula
02
What the data says
10 relationship studies, heat map, golden batch, best and worst days
03
How we built the models
Input data, split method, models compared, best model, evaluation, Databricks
04
What the operator gets
Setpoints with historical ranges, every reversal cycle and every hour
05
Delivering the 2%
Path to target, trial plan, measurement and verification
Notes: Five parts: the challenge, what the data told us, how we built and tested the models, what the operator receives, and how the 2% is delivered and measured.

## Slide 3: Executive summary
Run the recommended setpoints and SFC comes down, every month we tested
1,576.6
kcal/kg baseline rebuilt from raw 15-min data (client: 1,576.3)
−1.27%
SFC with the recommended setpoints, Jun–Aug 2026 (1,605 → 1,585 kcal/kg)
10 / 10
months where the recommender beat actual operation (292 days replayed)
−2%
SFC reached by adding three trial levers on top of the recommender
Draw, furnace age and how gas, air and boost are set decide SFC.
We control the third: the recommender delivers the exact heat the furnace needs, compensates every NCV change instantly, and uses barrier boost only as much as the bottom temperature needs.
Every number was tested walk-forward (the model only ever saw earlier days) and every setpoint stays inside the furnace's own historical P1–P99 range.
Two models run in Databricks: gas + secondary air every 20-min reversal cycle, barrier boost every hour, delivered to the operator with the historical range beside each value.
Notes: Headline: we rebuilt the client baseline from raw data to within 0.3 kcal/kg, the recommended setpoints cut SFC by 1.27% on summer 2026 and beat actual operation in every one of the 10 months replayed. With three trial levers on top, the plan reaches 2%.

## Slide 4: The challenge
01
What the plant asked for and how success is measured

## Slide 5: Problem statement
Energy is set by experience today; gas quality and furnace state change faster than manual adjustments
Gas quality swings
NCV moves between 8,969 and 10,253 kcal/SCM (P5–P95), a 14% swing. Operators correct only 17% of the needed NG change in the same hour.
Boost set by feel
Barrier boost is used as a heat source, but 1 Gcal of boost replaces only 0.77 Gcal of gas. More boost than the bottom needs raises SFC.
Excess air
Every extra 0.01 SCM of air per Mcal costs ≈ 0.13 Gcal/day; the heat leaves through the regenerators.
Furnace ageing
Energy at the same draw rises ≈ 0.19% per month, so standing still means SFC creeps up.
The goal
−2%
SFC of the melter (NG + melter boost + barrier boost), forehearths excluded
1,576.3 → 1,544.8
kcal/kg, baseline 1 Sep 2025 – 31 Jul 2026. Seeds and furnace limits must hold.
Notes: Four sources of waste we found in the data: slow NCV compensation, boost used as a heat source, excess air, and ageing. The goal is a 2% lower melter SFC versus the client baseline of 1,576.3 kcal/kg.

## Slide 6: Acceptance criteria
Two recommenders, one success yardstick, quality and furnace limits as hard guard-rails
Model 1: Gas recommender
Every 20-min reversal (ready by minute 15)
Inputs: NCV (UEMS, 15 min), draw and cullet (day), actual boost (DB)
Recommends: NG flow (one value for both ports), secondary air, air-fuel ratio
Unit = workbook unit, so the operator types the value directly
Model 2: Barrier-boost recommender
Every hour
Input: MB3 bottom temperature (DCS) and last hour's boost
Recommends: barrier boost (kWh/h) that holds MB3 at its target
Melter boost stays on its fixed levels (known input)
Success is accepted when
−2% per 5-t draw band, or
−2% draw-adjusted vs the baseline model at the same draw and cullet
Seeds within spec (≤ 30) every day
All setpoints inside the historical P1–P99 limits until the plant issues official ones
Optical crown temperature monitored as a guard-rail (1,568–1,578 °C)
Notes: The plant asked for two models: gas every reversal cycle and barrier boost every hour. Success is −2% per draw band or draw-adjusted, with seeds and limits respected.

## Slide 7: SFC formula and baseline
We use the client formula exactly, and rebuilt the client baseline from raw data
SFC (kcal/kg) = [ Σ NG × NCV + ( Σ Barrier kWh + Σ Melter kWh ) × 860 ] ÷ Draw (kg)
per day | NG × NCV computed every 15 minutes, then summed (never daily NG × average NCV) | 860 kcal per kWh
84%
of melter energy is gas (NG × NCV)
16%
is electricity (barrier + melter boost)
≈ 60%
of daily energy is fixed heat loss, independent of draw
Baseline check
Client baseline 1,576.3 kcal/kg
Our recomputation 1,576.6 kcal/kg
Target (−2%) 1,544.8 kcal/kg
Difference 0.02%: the data foundation matches the client's books.
Draw-adjusted yardstick (Model A, fitted on 286 baseline days): E_expected (Gcal/day) = 53.55 + 0.605 × draw (t) + 0.123 × cullet %. Draw-adjusted % = actual energy ÷ E_expected − 1.
Notes: The formula is the client's. We sum NG times NCV every 15 minutes. Recomputed from raw data, the baseline is 1,576.6 vs the client's 1,576.3. The draw-adjusted yardstick compares each day with what the baseline furnace would have used at the same draw and cullet.

## Slide 8: What the data says
02
395 days, 37,920 fifteen-minute records, 10 relationships that drive SFC

## Slide 9: 1. SFC history month by month
SFC follows draw: low-draw months (Feb, Jun, Jul 2026) carry the highest SFC
Chart: Average daily SFC, kcal/kg (usable days)
| Oct 25 | Nov 25 | Dec 25 | Jan 26 | Feb 26 | Mar 26 | Apr 26 | May 26 | Jun 26 | Jul 26 | Aug 26 | Sep 26
Monthly SFC | 1532.3 | 1564.9 | 1556.5 | 1559 | 1597 | 1580.3 | 1571.8 | 1552.6 | 1611.9 | 1640.2 | 1569.5 | 1610.4
Client baseline 1,576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3 | 1576.3
Chart: Average draw, t/day
| Oct 25 | Nov 25 | Dec 25 | Jan 26 | Feb 26 | Mar 26 | Apr 26 | May 26 | Jun 26 | Jul 26 | Aug 26 | Sep 26
Draw | 58.3 | 58.3 | 59 | 58.1 | 55.9 | 57.1 | 57.8 | 59 | 56.2 | 55.3 | 59.8 | 57.2
343
usable days analysed (NCV ≥ 90% valid, data ≥ 90%, draw present)
1,640
kcal/kg in Jul 2026 at 55.3 t/day, the highest month
1,533
kcal/kg in Oct 2025 at 58.3 t/day, the lowest month
Notes: Monthly SFC against the client baseline. The months with the highest SFC are the months with low draw, which sets up the first relationship.

## Slide 10: 2. Draw is the strongest driver of SFC
+1 t/day of draw lowers SFC by about 1%; 60% of the melter's energy is fixed
Chart: Daily SFC vs draw, 343 usable days
r = −0.92
correlation of draw with SFC
54 Gcal
per day fixed heat loss + 0.63 Gcal per tonne drawn
≈ −1%
SFC for every extra 1 t/day of draw
Notes: Energy is about 54 Gcal per day of fixed losses plus 0.63 Gcal per tonne. Because the fixed part is spread over the tonnes drawn, one more tonne per day cuts SFC by about 1%. This is why every comparison must be draw-adjusted.

## Slide 11: 3. SFC by draw band
Each 5-t band has its own baseline; the 55–65 t bands cover 80% of days
Chart: Average SFC per draw band, kcal/kg
| 45-50 t | 50-55 t | 55-60 t | 60-65 t
SFC | 1763 | 1668 | 1570 | 1529
Band | Days | SFC | Baseline | Target −2%
45-50 t | 7 | 1,763 | 1,765.9 | 1,730.6
50-55 t | 59 | 1,668 | 1,664.0 | 1,630.7
55-60 t | 174 | 1,570 | 1,566.7 | 1,535.4
60-65 t | 103 | 1,529 | 1,521.5 | 1,491.1
Energy per day rises only 7.2 Gcal (8%) from the lowest to the highest band, while draw rises 27%.
Band targets let each day be judged against days with the same draw.
Keeping draw at or above 55 t/day is itself one of the strongest SFC levers.
Notes: Splitting by 5-tonne draw band gives a fair target per band. Band baselines from the client baseline period, target −2% in each.

## Slide 12: 4. Furnace ageing adds energy every month
At the same draw and cullet, energy rises ≈ 0.19% per month (p ≈ 0.003)
Chart: Energy vs baseline model at the same draw and cullet, %
| Oct 25 | Nov 25 | Dec 25 | Jan 26 | Feb 26 | Mar 26 | Apr 26 | May 26 | Jun 26 | Jul 26 | Aug 26 | Sep 26
Draw-adjusted | -2.1 | 0.3 | 0.4 | -0.3 | -0.3 | 0.1 | -0.1 | 0 | 0.4 | 1.2 | 1.8 | 1.7
+0.19%
energy per month at the same draw (regenerator and refractory wear)
+1.1%
Jun–Aug 2026 above the draw-adjusted baseline
The gas model includes furnace age, so its target moves with the furnace instead of chasing an old state.
Notes: Draw-adjusted energy month by month. Above zero means more energy than the baseline furnace at the same draw. The trend is about +0.19% per month. The model carries an age term so the targets stay realistic.

## Slide 13: 5. NCV changes are corrected late
Operators make only 17% of the needed NG change in the same hour; exact compensation makes it 100%
Chart: Share of the needed NG correction made after an NCV change, %
| Same hour | After 1 h | After 2 h | Later
Correction | 17 | 73 | 89 | 80
8,969 – 10,253
kcal/SCM NCV range (P5–P95): the same SCM of gas carries up to 14% more or less heat
What it costs
When NCV rises, the furnace gets more heat than needed for 1–2 hours; when it falls, the crown is short and gets over-corrected later.
The recommender sets NG = heat target ÷ latest NCV every cycle, so the delivered heat stays on target.
Notes: When NCV changes, the gas flow should change by the inverse ratio. Operators make 17% of that change in the same hour and 73% after one hour. The recommender uses the latest NCV every reversal, so the heat delivered is exact.

## Slide 14: 6. Barrier boost controls the bottom temperature
+100 kWh/h of barrier boost raises MB3 by 1.9 °C within 6–12 hours; the same heat as gas moves it only 0.4 °C
Chart: MB3 rise after a +100 kWh/h step in barrier boost, °C
| 0 h | 1 h | 2 h | 3 h | 4 h | 5 h | 6 h | 7 h | 8 h | 9 h | 10 h | 11 h | 12 h
MB3 response | 0 | 0 | 0.12 | 0.57 | 0.94 | 1.19 | 1.38 | 1.55 | 1.69 | 1.77 | 1.83 | 1.91 | 1.94
+1.9 °C
MB3 per +100 kWh/h of barrier boost (steady state)
+0.4 °C
MB3 for the same heat delivered as gas
Estimated with a 0–12 h distributed-lag model on 6,736 hours, so operator feedback does not bias the result.
Notes: Barrier boost is the handle for the bottom temperature MB3. The response builds over 6 to 12 hours. Gas barely moves MB3. This is why the second model controls boost from MB3.

## Slide 15: 7. Boost is a temperature handle, not an energy saver
1 Gcal of barrier boost replaces only 0.77 Gcal of gas, so extra boost raises SFC
Add 1 Gcal of barrier boost …
+1.00 Gcal electricity in
−0.77 Gcal gas saved
Net +0.23 Gcal more energy
0.77 (chosen gas model) to 0.83 (month fixed effects) Gcal gas per Gcal of boost, ageing controlled
What it means
Use the minimum boost that holds MB3 at its target, not more.
In Jun–Aug 2026 MB3 ran 1.5 °C above its historical median: boost was higher than the glass needed.
The boost controller trims it hour by hour; if NG is already at its upper limit, boost is not lowered.
Notes: Electric boost is more efficient per unit, but in this furnace one Gcal of boost replaced only 0.77 Gcal of gas once ageing is controlled. So more boost raises total energy. The right policy is the minimum boost that holds MB3.

## Slide 16: 8. Less air per unit of heat means less energy
Days with the lowest air per Mcal used about 1% less energy than the highest-air days at the same draw
Chart: Energy vs baseline at the same draw, by air per Mcal quarter, %
| Lowest air 1.247 | Q2 1.263 | Q3 1.272 | Highest air 1.288
Draw-adjusted | -0.24 | -0.01 | 0.63 | 0.79
1.27 SCM/Mcal
average secondary air per Mcal of gas heat
≈ 0.13 Gcal/day
saved for every 0.01 SCM/Mcal less air (p ≤ 0.01, inside history)
Air follows heat (R² 0.66), not gas volume (R² 0.44), so the recommender sets air per Mcal × heat and derives the AFR from it.
Notes: Secondary air that is not needed for combustion is heated and leaves through the regenerators. Splitting days by air per Mcal shows the lowest quarter used less energy than baseline, the highest quarter more. The recommender targets the 25th percentile of the last 45 days, never below the historical 5th percentile.

## Slide 17: 9. Glass quality has headroom
Seeds never exceeded the spec of 30 on usable days, and efficient days have fewer seeds
Chart: Days by daily seed count (spec: 30 each)
| 6–10 | 11–15 | 16–20 | 21–25 | 26–30
Days | 40 | 167 | 113 | 21 | 2
15
median seeds
21
P95 seeds
28
maximum (spec 30)
13.6
seeds on the most efficient days (15.6 on the least)
Lower energy has not cost quality: the seed guard-rail (> 21 on 2 days, or any day > 25) is built into the trial.
Notes: Seeds are the quality guard-rail. On usable days the 95th percentile is 21 and the maximum 28, below the spec of 30. Efficient days actually have fewer seeds.

## Slide 18: 10. Crown temperature is held flat
Optical crown is held within ±0.8 °C, 7.6 °C above the crown thermocouple; we use it as a guard-rail
Chart: Monthly average crown temperature, °C
| Sep 25 | Oct 25 | Nov 25 | Dec 25 | Jan 26 | Feb 26 | Mar 26 | Apr 26 | May 26 | Jun 26 | Jul 26 | Aug 26 | Sep 26
Optical crown (manual, hourly) | 1574.47 | 1574.78 | 1574.73 | 1574.76 | 1574.57 | 1574.41 | 1574.64 | 1574.73 | 1574.83 | 1574.53 | 1574.54 | 1574.26 | 1573.17
Crown TC MC3 (DCS, 1 min) | 1567.62 | 1568 | 1567.86 | 1567.38 | 1567.29 | 1566.99 | 1566.97 | 1566.58 | 1566.98 | 1566.7 | 1566.18 | 1566.07 | 1565.33
+7.6 °C
optical above TC MC3 (daily sd 0.8 °C), 9,372 hours compared
0.8 °C
daily spread of the optical reading: operators hold it flat
A flat signal cannot explain energy changes, so crown temperature is not a model input; the recommender flags any reading outside 1,568–1,578 °C.
Notes: The optical pyrometer is typed by hand hourly; the crown thermocouple is logged every minute. They agree on the daily level, with a 7.6 degree offset. Because the crown is held flat, it carries no information on energy; we keep it as a guard-rail. A 1–2 degree lower crown setpoint is one of the trial levers.

## Slide 19: Relationship heat map
Correlation between daily drivers (343 usable days): draw dominates, boost follows draw, AFR follows NCV
 | Draw | SFC | Gas heat | Elec heat | Barrier boost | Melter boost | NCV | Air/Mcal | AFR | MB3 bottom | Optical crown | Crown TC | Cullet % | Seeds
Draw | 1 | -0.92 | 0.23 | 0.84 | 0.84 | 0.37 | -0.04 | -0.05 | -0.06 | 0.26 | 0.21 | 0.19 | 0.02 | 0.06
SFC | -0.92 | 1 | 0.10 | -0.81 | -0.78 | -0.41 | -0.07 | 0.18 | -0.02 | -0.13 | -0.30 | -0.35 | 0.09 | 0.05
Gas heat | 0.23 | 0.10 | 1 | -0.15 | -0.04 | -0.32 | -0.07 | 0.30 | 0.02 | 0.35 | -0.25 | -0.50 | 0.36 | 0.23
Elec heat | 0.84 | -0.81 | -0.15 | 1 | 0.93 | 0.58 | -0.18 | -0.12 | -0.23 | 0.15 | 0.29 | 0.37 | -0.15 | 0.05
Barrier boost | 0.84 | -0.78 | -0.04 | 0.93 | 1 | 0.25 | -0.15 | -0.05 | -0.19 | 0.24 | 0.18 | 0.22 | -0.02 | 0.04
Melter boost | 0.37 | -0.41 | -0.32 | 0.58 | 0.25 | 1 | -0.13 | -0.21 | -0.21 | -0.12 | 0.37 | 0.50 | -0.37 | 0.04
NCV | -0.04 | -0.07 | -0.07 | -0.18 | -0.15 | -0.13 | 1 | -0.41 | 0.95 | 0.00 | 0.24 | 0.19 | 0.00 | -0.22
Air/Mcal | -0.05 | 0.18 | 0.30 | -0.12 | -0.05 | -0.21 | -0.41 | 1 | -0.12 | 0.17 | -0.12 | -0.33 | 0.34 | 0.18
AFR | -0.06 | -0.02 | 0.02 | -0.23 | -0.19 | -0.21 | 0.95 | -0.12 | 1 | 0.05 | 0.22 | 0.10 | 0.11 | -0.19
MB3 bottom | 0.26 | -0.13 | 0.35 | 0.15 | 0.24 | -0.12 | 0.00 | 0.17 | 0.05 | 1 | 0.13 | -0.03 | 0.12 | 0.12
Optical crown | 0.21 | -0.30 | -0.25 | 0.29 | 0.18 | 0.37 | 0.24 | -0.12 | 0.22 | 0.13 | 1 | 0.68 | -0.04 | -0.01
Crown TC | 0.19 | -0.35 | -0.50 | 0.37 | 0.22 | 0.50 | 0.19 | -0.33 | 0.10 | -0.03 | 0.68 | 1 | -0.27 | -0.07
Cullet % | 0.02 | 0.09 | 0.36 | -0.15 | -0.02 | -0.37 | 0.00 | 0.34 | 0.11 | 0.12 | -0.04 | -0.27 | 1 | 0.12
Seeds | 0.06 | 0.05 | 0.23 | 0.05 | 0.04 | 0.04 | -0.22 | 0.18 | -0.19 | 0.12 | -0.01 | -0.07 | 0.12 | 1
Read-outs
Draw vs SFC: −0.92
Draw vs barrier boost: +0.84, boost is raised with draw
NCV vs AFR: +0.95, air already follows heat
Gas heat vs crown TC: −0.50, operators fire to the crown
Cullet vs energy: no significant effect once age is controlled
Notes: Orange is positive, blue negative correlation. Draw dominates SFC. Boost follows draw. AFR follows NCV because air is set by heat. Correlations alone are not causal, so each lever was then tested with ageing controlled.

## Slide 20: Historical insights
Eight findings from 13 months of data shape the recommender
Draw
+1 t/day ≈ −1% SFC; 54 Gcal/day is fixed loss
Ageing
+0.19% energy per month at the same draw
NCV lag
17% corrected in the same hour, 73% after 1 h
Boost
1 Gcal boost replaces only 0.77 Gcal gas
MB3
+1.9 °C per +100 kWh/h barrier boost
Air
−0.01 SCM/Mcal ≈ −0.13 Gcal/day
Quality
Seeds P95 21, max 28, spec 30
Cullet
16–20% cullet: no significant energy effect
Notes: A one-page summary of what the data proved. Each finding was tested walk-forward and with ageing controlled before it was used in a model.

## Slide 21: Golden batch: what the best days do differently
The most efficient 25% of days (86 days) used ≈ 3% less energy than the least efficient 25% at the same draw
Daily average | Best 25% | All days | Worst 25%
Draw, t/day | 57.8 | 57.7 | 57.5
SFC, kcal/kg | 1,550 | 1,579 | 1,604
Energy vs baseline (draw-adjusted) | -1.35% | +0.29% | +1.64%
Secondary air per Mcal, SCM | 1.261 | 1.268 | 1.271
Melter boost, kWh/day | 7,603 | 7,688 | 8,036
Barrier boost, kWh/day | 8,726 | 8,822 | 8,801
MB3 bottom, °C | 1,320.0 | 1,320.5 | 1,320.7
Gas NCV, kcal/SCM | 9,807 | 9,613 | 9,415
Optical crown, °C | 1,574.6 | 1,574.5 | 1,574.5
Seeds | 13.6 | 14.8 | 15.6
Golden-day recipe
Leaner air: ≈ 1.26 SCM per Mcal
Bottom held near 1,320 °C, not hotter
≈ 430 kWh/day less melter boost
Gas matched to NCV (richer gas, less SCM)
Same crown temperature, fewer seeds
The recommender reproduces these days: its gas target is the level the best quarter of comparable days achieved.
Notes: Days are ranked by energy after removing draw, cullet and furnace age. The best quarter runs leaner air, a cooler bottom, less melter boost, and keeps the same crown temperature with fewer seeds. This is the golden batch the gas model targets.

## Slide 22: Lowest vs highest SFC days: what happened
The extremes are set by draw: the lowest-SFC days ran 60–61.5 t, the highest ran below 51 t
5 lowest-SFC days
Date | Draw t | SFC | Gas Gcal | Barrier kWh | MB3 °C | Seeds
2025-10-20 | 60.2 | 1,483 | 72.6 | 11,333 | 1,319.7 | 10
2026-01-24 | 61.5 | 1,488 | 74.6 | 12,292 | 1,324.3 | 14
2025-10-17 | 60.2 | 1,488 | 72.8 | 12,208 | 1,319.2 | 11
2025-10-16 | 59.7 | 1,490 | 73.5 | 10,633 | 1,318.6 | 11
2025-10-22 | 60.4 | 1,491 | 72.7 | 12,072 | 1,319.4 | 7
5 highest-SFC days
Date | Draw t | SFC | Gas Gcal | Barrier kWh | MB3 °C | Seeds
2026-06-25 | 47.8 | 1,787 | 77.5 | 3,381 | 1,319.4 | 14
2026-06-26 | 48.0 | 1,785 | 78.0 | 2,952 | 1,320.1 | 17
2026-06-27 | 47.8 | 1,769 | 77.5 | 2,602 | 1,320.6 | 12
2026-07-18 | 49.5 | 1,763 | 76.8 | 4,825 | 1,318.3 | 12
2026-09-23 | 50.6 | 1,754 | 77.6 | 6,885 | 1,317.1 | 11
Lowest SFC: 1,483–1,491 kcal/kg
Oct 2025 and Jan 2026, draw 60–61.5 t/day
Gas only 72.6–74.6 Gcal/day, air per Mcal 1.25–1.26
Seeds 7–14: quality was better, not worse
Highest SFC: 1,754–1,787 kcal/kg
25–27 Jun 2026 at 47.8 t/day, the lowest draw of the year
Draw fell 17% but gas stayed at 77.5 Gcal/day: the fixed heat loss is spread over fewer tonnes
Barrier boost was cut to 2,600–3,400 kWh/day
Notes: Raw SFC extremes are mostly a draw story. The lowest days were high-draw days in October 2025 and January 2026; the highest were the low-draw days at the end of June 2026. This is why we judge operation draw-adjusted, next slide.

## Slide 23: Same draw, different SFC: operation makes the gap
At similar draw, the best and worst days differ by up to 11 Gcal/day of gas: the part the recommender controls
Best days (draw-adjusted)
Date | Draw t | SFC | vs baseline | Gas Gcal | Barrier kWh | MB3 °C
2026-06-03 | 57.8 | 1,495 | -4.9% | 72.2 | 9,257 | 1,322.4
2026-04-23 | 56.7 | 1,515 | -4.8% | 72.4 | 8,416 | 1,319.5
2026-02-24 | 55.2 | 1,538 | -4.5% | 72.5 | 7,204 | 1,319.8
2025-10-11 | 53.8 | 1,588 | -3.4% | 72.7 | 6,749 | 1,319.0
Worst days (draw-adjusted)
Date | Draw t | SFC | vs baseline | Gas Gcal | Barrier kWh | MB3 °C
2026-06-29 | 57.3 | 1,670 | +5.7% | 83.2 | 7,346 | 1,318.1
2026-08-19 | 61.9 | 1,581 | +4.8% | 82.2 | 10,867 | 1,324.6
2026-08-20 | 61.6 | 1,578 | +4.3% | 81.7 | 10,623 | 1,324.2
2026-08-07 | 60.5 | 1,586 | +3.8% | 80.2 | 11,148 | 1,322.4
19–20 Aug 2026: what happened
MB3 was already 4 °C above its median, yet barrier boost was raised to 10,600–10,900 kWh/day
NG pushed to 102–109 SCM/15 min (above its P99 of 96) and gas reached 82 Gcal/day
Seeds rose to 28 on 20 Aug
Recommender replay on the same days
SFC 1,581 → 1,507 and 1,578 → 1,511 kcal/kg (−4.7% and −4.3%), boost 453 → 265 kWh/h
Notes: Once draw is taken out, the spread is operation. The worst days in August 2026 over-fired both gas and boost while the bottom was already hot. In the walk-forward replay the recommender would have run those days 4–5% lower.

## Slide 24: How we built the models
03
Input data, split method, models compared, the chosen model, evaluation and deployment

## Slide 25: Input data
Four client files; one corrected 15-min record drives every calculation
File | Sheet | Frequency / period | Size | Used for
Analytical_Record_Creation_fixed_5.xlsx | result | 15 min, 1 Sep 2025 – 30 Sep 2026 | 37,920 rows | All models (main record)
DCS_60_TPD_MelterCrown3.xlsx | first sheet (TC MC3) | 1 min, 1 Sep 2025 – 1 Oct 2026 | ≈ 570,000 rows | Crown checks
SFC_60_TPD_Baseline_Calculation_Sep-25_to_Jul-26_updated.xlsx | Master Data- Energy & SFC Calc | Daily, 1 Sep 2025 – 31 Jul 2026 | 334 days | Baseline verification only
Analytical_Record_Creation_EE_60TPD_updated-2.xlsx | result, Sheet1 | 15 min (first version) | 43,392 rows | Evidence for log corrections
Columns used from sheet result
NCV Meter
kcal/SCM
dcs_60_MelterGasflowvalue
NG, SCM/15 min
dcs_60_SecondaryAirFlowvalue
air, SCM/15 min
BARRIER BOOSTER-52
kWh/15 min
MELTER BOOSTER-51
kWh/15 min
dcs_60_ThermocoupleMelterBottom3
MB3, °C
Melter Optical Temperature
°C, hourly log
Daily Draw · Cullet % · Seed Count
daily
Notes: The corrected analytical record, sheet 'result', is the single source for every model. The crown thermocouple file is used for checks. The client baseline workbook is used only to verify our baseline, never as a model input.

## Slide 26: Data levels and cleaning
One cleaned 15-min record, rolled up to the level each model needs
15-min
37,920
records · Gas back-test, NG × NCV per interval
Hourly
9,480
hours · Boost controller: 6,736 hours with MB3 + boost
Daily
395
days · Gas target, SFC, M&V
Usable
343
days · 286 in the baseline period, 27 in Sep 2026
Cleaning rules (applied the same way live)
Rule | Affected | Action
NCV outside 8,500–10,500 or a spike > 400 from the 2-h median | 3,659 readings + 159 spikes | Set to missing; live: last valid NCV
Day with < 90% valid NCV | 46 days | Left out (no client NCV substituted)
SAP draw doubled on month-start days | 3 days | Halved (matches SAP exactly)
Boost, optical, crown TC out of range | zeros and glitches | Set to missing; gaps ≤ 1 h interpolated
Notes: Raw 15-minute data is cleaned once in one module and rolled up to hourly for the boost model and daily for the gas target and SFC. The same rules run on live data.

## Slide 27: Split method: walk-forward, never random
Each day is predicted only from days before it, exactly as the model will run live
Sep 25
Oct
Nov
Dec
Jan 26
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep 26
Fold 1
Train: all earlier days (expanding)
Test Mar–May 26
Fold 2
Train: all earlier days (expanding)
Test Jun–Aug 26
Unseen
Train: everything up to Aug 2026
Sep 26
Replay
Full recommender replayed day by day: 292 days, Dec 2025 – Sep 2026
Why not random?
A random split leaks future furnace states (ageing, NCV, draw) into training and overstates accuracy.
Refit every day
The gas model is refit on all past days each day, like the live daily retraining job.
Calibration checked
The target should be beaten on 25% of days; we check this out of sample in every fold.
Notes: Two walk-forward folds for model selection, Sep 2026 held back as an unseen month, and a full day-by-day replay of the final recommender over 292 days. The model never sees the day it predicts.

## Slide 28: Gas models compared
Eight model types × input sets, scored on two walk-forward folds (Mar–May and Jun–Aug 2026)
Model | Pinball loss | Days below target (25% ideal) | MAE Gcal/d | Verdict
OLS expanding + ageing + efficiency shift | 0.344 | 20–30% | 0.94 | Chosen: calibrated, transparent
Quantile regression expanding + ageing | 0.331 | 15–28% | 0.98 | Too ambitious (15% of days)
OLS rolling 45 d + efficiency shift | 0.362 | 22–28% | 1.03 | Less accurate
LightGBM expanding + ageing | 0.362 | 16–26% | 1.09 | Black box, not more accurate
Quantile regression rolling 60 d | 0.367 | 11–21% | 1.17 | Unrealistic target
Quantile regression rolling 45 d (first version) | 0.386 | 25–28% | 1.13 | Less accurate
Quantile regression rolling 30 d | 0.394 | 22–28% | 1.13 | Less accurate
LightGBM expanding (no age) | 0.442 | 4–16% | 1.59 | Fails: cannot extrapolate ageing
Inputs tested
Barrier boost: needed (loss 0.437 without it)
Melter boost: kept (0.345 without)
Optical crown, yesterday: no gain (0.344)
Crown TC, MB3, cullet: no reliable gain
Hourly model: R² 0.18, mostly operator reaction
Notes: Pinball loss measures how well a model hits the 25th-percentile efficient target. The quantile model scores slightly lower loss but only 15% of days beat its target, so it would ask too much. The OLS model with ageing and a 45-day efficiency shift is calibrated in every fold and fully transparent.

## Slide 29: Air and boost models compared
Air follows heat; an integral controller holds MB3 best with calm moves
Secondary air: 4 formulas
Formula | Error / fit | Verdict
Constant air-fuel ratio | 3.3% | Ignores NCV
Air per gas volume | R² 0.44 | Ignores NCV
Air per Mcal of heat | 1.5% (R² 0.66) | Chosen
OLS on heat + NCV | similar | More complex, no gain
Target: P25 of the last 45 days' air per Mcal, floor at the historical P5 (1.226). No O₂ analyser, so the target stays inside proven history.
Barrier boost: 4 policies, closed-loop replay Jun–Aug 2026
Policy | MB3 error °C | Boost kWh/h | Move kWh/h | Energy Gcal/d
Copy operators (OLS) | 1.42 | 321 | 11.1 | −0.12
Copy operators (LightGBM) | 1.39 | 324 | 13.6 | −0.11
Integral controller on MB3 | 1.09 | 268 | 5.4 | −0.37
Hybrid (feedforward + integral) | 1.12 | 266 | 6.2 | −0.38
Integral controller: lowest MB3 error in both folds (1.05 °C and 1.09 °C) with the calmest hourly moves.
The operator-copy regression was unstable: its MB3 coefficient moved from −0.6 to −22 between windows.
Melter boost adds nothing to the controller (MB3 forecast 0.540 → 0.537), so it is left out.
Notes: Air: the error of a fixed air-fuel ratio is twice that of air per Mcal. Boost: four policies were replayed closed-loop. The integral controller holds MB3 best, moves boost gently, and saves about 0.37 Gcal per day.

## Slide 30: The final model
Three transparent equations, refit daily on all past usable days
Gas heat target (daily)
Gas heat (Gcal/day) = 52.19 + 0.495 × draw (t) − 0.771 × barrier boost (Gcal) − 0.099 × melter boost (Gcal) + 0.350 × furnace age (months) − 0.41 efficiency shift
NG (SCM/15 min) = gas heat × 10⁶ ÷ 96 ÷ latest NCV
Secondary air and AFR
Secondary air (SCM/15 min) = 1.268 SCM/Mcal × heat per 15 min (Mcal)
AFR = secondary air ÷ NG. Air target = P25 of last 45 days, floor 1.226
Barrier boost (hourly)
Boost(t) = Boost(t−1) + 0.1 × (1,320.25 − MB3) ÷ 0.0194 °C per kWh/h
Clipped to 114–610 kWh/h. Not lowered if NG is at its upper limit
Signs are physical: more draw needs more heat; boost replaces part of the gas; the aging furnace needs +0.35 Gcal/day per month. Every setpoint is clipped to the historical P1–P99.
Notes: The final model is three equations an engineer can check by hand. Gas: OLS with draw, barrier and melter boost and furnace age, shifted to the efficient quarter of the last 45 days. NG is heat divided by the latest NCV. Air is air per Mcal times heat. Boost is an integral controller on MB3.

## Slide 31: Model evaluation: summer 2026
Walk-forward on Jun–Aug 2026 (85 days): each step lowers SFC, all setpoints inside history
Chart: Average SFC, kcal/kg
| Actual operation | Gas model | + Boost controller | + Air target
SFC | 1605.3 | 1594 | 1587.7 | 1585
Step | SFC vs actual | Draw-adjusted
Gas model | −0.70% | +0.42%
+ Boost controller | −1.09% | +0.01%
+ Air target | −1.27% | −0.17%
Per draw band (vs band baseline)
Band | Actual | Recommended
45–50 t (5 days) | +0.23% | −0.62%
50–55 t (18 days) | +1.36% | +1.23%
55–60 t (33 days) | +1.36% | −0.26%
60–65 t (29 days) | +1.60% | −0.15%
Draw-adjusted: +1.14% actual → −0.17%. 15-min back-test with exact NCV gives 0.81% for gas alone (8,092 recommendations).
Notes: Each step was simulated walk-forward. Gas alone saves 0.70%, the boost controller takes it to 1.09%, the air target to 1.27%. In the two most common draw bands, SFC moves from about 1.5% above the band baseline to below it.

## Slide 32: Model evaluation: every month, and an unseen month
Replayed day by day over 292 days, the recommender beat actual operation in all 10 months
Chart: Average SFC by month, kcal/kg
| Dec 25 | Jan 26 | Feb 26 | Mar 26 | Apr 26 | May 26 | Jun 26 | Jul 26 | Aug 26 | Sep 26
Actual | 1557 | 1559 | 1597 | 1580 | 1572 | 1553 | 1612 | 1640 | 1570 | 1610
Recommended | 1551 | 1546 | 1567 | 1574 | 1565 | 1545 | 1591 | 1625 | 1545 | 1602
1,583 → 1,570
kcal/kg over 292 days (−0.86%), Dec 2025 – Sep 2026
0.3–1.9%
lower SFC in every month (best: Feb 2026 1.9%, Aug 2026 1.5%)
26%
of unseen Sep 2026 days beat the gas target (25% designed): calibrated
Notes: The full recommender replayed on every usable day from December 2025, each day using only earlier data. It is lower than actual in every month. On the unseen September 2026 the gas model stayed calibrated.

## Slide 33: Packaged in Databricks
Two scheduled jobs: daily retraining and live recommendations to the operator
Plant data
DCS (MB3, NG, air) · UEMS NCV (MQTT) · SAP draw · boost DB
Job 01: training
Daily 06:30 · clean → daily/hourly → fit gas, air, boost, limits, M&V
Job 02: inference
Every 20 min (gas, air) · hourly (boost) · limit + freshness checks
Quality gate
Signs, ranges, 30-day coverage 10–45%: release only on pass
Operator e-mail
Setpoints + historical range via plant Logic App; log to Delta
Operator
Sets NG and air in minute 15–20; boost each hour
Model file sfc_recommender_latest.json (numbers only, versioned) · Notebooks 01_training_sfc_model and 02_inference_recommendation_email · pandas/numpy only, no project code needed
Notes: Job 01 retrains daily after SAP draw arrives and releases the model only if the checks pass. Job 02 loads the released model, reads the latest plant values, checks limits and data freshness, and e-mails the operator via the plant's Logic App, logging each recommendation.

## Slide 34: What the operator gets
04
Four setpoints, each shown with its historical range

## Slide 35: Operator setpoints
Every value is in the same unit as the DCS / workbook column: the operator types it directly
NG flow
SCM/15 min
One value for both ports (common header)
Every 20-min reversal, set in minute 15–20
Secondary air
SCM/15 min
Air per Mcal × heat
Every 20-min reversal
Air-fuel ratio
air ÷ NG
Follows NCV automatically
Every 20-min reversal
Barrier boost
kWh/h
Holds MB3 at 1,320.25 °C
Every hour
Automatic inputs
NCV every 15 min (UEMS); spikes filtered, last valid value kept
MB3 bottom temperature and last hour's boost (DCS / DB)
Operator inputs (once a day / hourly)
Draw and cullet % for the day
Optical crown temperature: checked against 1,568–1,578 °C as a guard-rail
Notes: The operator receives four numbers. NG, air and AFR every reversal, ready by minute 15. Barrier boost every hour. Inputs are mostly automatic; the operator only confirms draw, cullet and the optical reading.

## Slide 36: Historical range + recommendation
Example: 19 Aug 2026, 10:00. The furnace was over-fired; the recommendation brings every setpoint back inside history
Inputs: NCV 9,117 kcal/SCM · draw 61.9 t · cullet 19% · MB3 1,323.7 °C · barrier boost last hour 563 kWh/h · optical 1,574.5 °C (in band)
Setpoint
Historical P1 – P99 range (grey), median (|), actual (●), recommended (◆)
Actual
Recommended
NG flow
SCM/15 min
73.9
96.3
105.5 ▲ >P99
87.9
Secondary air
SCM/15 min
921
1,104
1,196 ▲ >P99
1,015
Air-fuel ratio
–
10.99
13.44
11.34
11.56
Barrier boost
kWh/h
114
610
618 ▲ >P99
545
Result for the day (walk-forward replay): SFC 1,581 → 1,507 kcal/kg (−4.7%). Barrier boost steps down each hour as MB3 returns to 1,320 °C.
Notes: This is what the operator sees: each setpoint with its historical P1–P99 range and median. On 19 August at 10:00 the furnace ran NG and air above their historical P99 and boost at its maximum while MB3 was already hot. The recommendation sits inside history and would have cut that day's SFC by 4.7%.

## Slide 37: Delivering the 2%
05
Recommended setpoints first, then three trial levers, measured every day

## Slide 38: Path to 2% lower SFC
Run the recommended setpoints, then add three trial levers, one at a time
SFC reduction vs today's operation at the same draw, %
Gas recommender
−0.72%
Barrier-boost controller
−0.41%
Air target (rolling P25)
−0.18%
Lever A: MB3 target → 1,319.2 °C
−0.30%
Lever B: air → 1.252 SCM/Mcal
−0.25%
Lever C: crown −1 to −2 °C
−0.15% or more
Total
−2.0%
Proven: walk-forward on Jun–Aug 2026. Trial: inside the historical range, confirmed in the trial phase.
Extra lever
+1 t/day
of draw ≈ −1% SFC. Holding ≥ 58 t/day multiplies the saving.
Regenerator maintenance recovers the ageing drift (+0.19%/month).
Notes: The proven part, 1.31%, comes from running the recommended gas, air and boost. Three trial levers add the rest, each kept inside the furnace's own history: MB3 target at its historical P25, air per Mcal at its historical P25 with an O2 spot check, and a 1-2 degree lower crown setpoint. Draw and maintenance add on top.

## Slide 39: Trial plan and measurement
Four phases over about 14 weeks, with daily guard-rails and daily M&V
Phase 0: Shadow
Weeks 1–2
Recommendations logged, not applied; data feeds checked
0%
Phase 1: Gas + air
Weeks 3–6
Operators set NG and secondary air each reversal
≈ −0.9%
Phase 2: + Boost
Weeks 7–10
Barrier boost from the MB3 controller
≈ −1.3%
Phase 3: Levers
Weeks 11–14
MB3 target, air per Mcal, crown setpoint, one at a time
≈ −2.0%
Phase 4: Lock-in
After
Final settings become SOP; 30 days of M&V
≥ −2%
Daily M&V
SFC with the client formula, draw-adjusted % and band %
CUSUM chart of the daily saving; weekly review with the process head
30 trial days measure the saving to ±0.74% (95% confidence)
Guard-rails (any breach → step back)
Seeds > 21 on 2 days, or any day > 25
MB3 outside 1,317.6–1,323.9 °C for > 3 hours
Optical crown below 1,570 °C; crown TC −3 °C vs last week
Notes: The trial starts in shadow mode so operators see the recommendations before using them. Gas and air come first, then boost, then the levers one at a time. Every day is measured with the client formula and the draw-adjusted yardstick; 30 days give a ±0.74% confidence band.

## Slide 40: Run the recommended setpoints, lower the SFC
Next steps: October data · official limits · O₂/CO analyser · shadow phase
−1.27%
SFC from the recommended setpoints (summer 2026)
10 / 10
months better than actual operation
−2%
with the three trial levers
Notes: Close: the recommender is built, tested on 13 months of data, packaged in Databricks and ready for the shadow phase. What we need from the plant: October data, official limits, an O2/CO analyser for lever B, and a start date.